## Slide 1
HOME AUTOMATION SYSTEM
TEAM MEMBERS:-
DEEPAK J PUTHUKKADEN-20
GIRIDHAR A K-31
GOVINDH B-32
ROHIT SREEKUMAR-53
SHINE ALI-59

## Slide 2
INTRODUCTION
A simple home automation project using raspberry pi,designed to perform a few basic functions in an household which include :-
Adaptive internal lighting system
External lighting system
Automatic water pump system
Password assisted door-locking system
Temperature measurement
Music system
Data logging

## Slide 3
BLOCK DIAGRAM
RASPBERRY PI
MICROCONTROLLER
WATER PUMP
I/P- 2 DIGITAL PINS
O/P- DIGITAL (STATUS LED)
PINS - 4
RTC MODULE
PINS – 2
TEMP MEASUREMENT
I/P – 1 ANALOG(LM35)
PINS - 1
MUSIC PLAYER
I/P- 4 BUTTON
O/P – LCD
PINS - 10
serial
DOOR LOCK
I/P- 4*3 KEYPAD
O/P- DIGITAL(STATUS LED)
PINS - 9
EXTERNAL LIGHTING
I/P- 1 ANALOG(LDR)
2 DIGITAL
O/P- 1 DIGITAL(LED)
PINS - 4
INTERNAL LIGHTING
I/P- 1 ANALOG(LDR)
2 DIGITAL
O/P- 1 PWM
PINS - 4
I2C

## Slide 4
SCHEDULE

## Slide 5
WORK PROGRESS

## Slide 6
EXTERNAL LIGHTING SYSTEM
DESCRIPTION:-
It controls an external lighting system based on the time of the day. The time is obtained via an RTC chip(DS1307) interfaced with Raspberry Pi.
PROGRESS:-
CODING – COMPLETED
DESIGN – COMPLETED
INTERFACING – ON PROGRESS

## Slide 7
EXTERNAL LIGHTING SYSTEM - CODE
#define elinput A0 #define eloutput 9 #define treshold 500 #define elinterrupt A1 #define eloverride A2 int elsensor,elstate; void setup() { Serial.begin(9600); pinMode(eloutput,OUTPUT); pinMode(elinterrupt,INPUT); pinMode(eloverride,INPUT); elstate=0; } | void loop() { elsensor=analogRead(elinput); if((elsensor>treshold) && (elstate==0)) { digitalWrite(eloutput,HIGH); Serial.println("External light is ON"); elstate=1; } else if((elsensor<treshold) && (elstate==1)) { digitalWrite(eloutput,LOW); Serial.println("External light is OFF"); elstate=0; } while(digitalRead(elinterrupt)) //interrupt function digitalWrite(eloutput,digitalRead(eloverride)); Serial.println("External light is ON-Override"); delay(500); }

## Slide 8
INTERNAL LIGHTING SYSTEM - DESIGN

## Slide 9
WATER PUMPING SYSTEM
DESCRIPTION:-
It controls the water pump based on water level in the tank.Prevents wastage of water.Using 2 sensors water level is determined and its output is used by Pi to drive the relay.
PROGRESS:-
CODING – COMPLETED
DESIGN – COMPLETED
INTERFACING – ON PROGRESS

## Slide 10
WATER PUMP SYSTEM - CODE
#define pcinput A0 #define pcoutput 9 #define pclinterrupt A1 #define pcloverride A2 int pcsensor,pcstate; void setup() { Serial.begin(9600); pinMode(pcinput,INPUT); pinMode(pcoutput,OUTPUT); pcsensor = digitalRead(pcinput); pcstate = pcinput; } | void loop() { pcsensor = digitalRead(pcinput); if(pcsensor!=pcstate) { if(pcsensor == 1) { digitalWrite(pcoutput,HIGH); Serial.println("Motor is ON"); pcstate = pcsensor; } else { digitalWrite(pcoutput,LOW); Serial.println("Motor is OFF"); pcstate = pcsensor; } } while(digitalRead(pcinterrupt)) //interrupt function digitalWrite(pcoutput,digitalRead(pcoverride)); delay(500); }

## Slide 11
WATER PUMP SYSTEM - DESIGN

## Slide 12
INTERNAL LIGHTING SYSTEM
DESCRIPTION:-
It controls the amount of illumination in a room based on the external inputs about the amount of sunlight entering a room.For,demonstration we use an LED,brightness of which is controlled using PULSE WIDTH MODULATION technique.
PROGRESS:-
CODING – COMPLETED
DESIGN – COMPLETED
INTERFACING – ON PROGRESS

## Slide 13
INTERNAL LIGHTING SYSTEM - CODE
#define alinput A0 #define aloutput 9 #define alinterrupt A1 #define aloverride A2 float alsensor,alvoltage; int albrightness; void setup() { Serial.begin(9600); pinMode(alinterrupt,INPUT); pinMode(aloverride,INPUT); } | void loop() { alsensor = analogRead(alinput); //read the sensor value albrightness = alsensor / 4; //convert the value to 8-bit res alvoltage = alsensor * (5.0 / 1024.0); //convert to 0-5V range Serial.print("The voltage is: "); //prints the voltage through serial Serial.println(alvoltage); analogWrite(aloutput,albrightness); //output the PWM to the LED while(digitalRead(alinterrupt)) //interrupt function { if(digitalRead(aloverride)) //override - ON analogWrite(aloutput,255); else //override - OFF analogWrite(aloutput,0); } delay(500); }

## Slide 15
DOOR-LOCKING SYSTEM
DESCRIPTION:-
Adds security to our home. Keypad is interfaced with a microcontroller which is then connected to a DOOR-LOCK system
PROGRESS:-
CODING – ON PROGRESS
DESIGN – ON PROGRESS
INTERFACING – ON PROGRESS

## Slide 16
MUSIC PLAYER SYSTEM
DESCRIPTION:-
It adds entertainment to our home. Music player is integrated into the Raspberry Pi which can play music using an installed software in the operating system.
PROGRESS:-
CODING – ON PROGRESS
DESIGN – ON PROGRESS
INTERFACING – ON PROGRESS

## Slide 17
CONCLUSION
70% of our project on HOME AUTOMATION is completed and the remaining 40% will be completed well before the submission date.

## Slide 18
THANK YOU